## Slide 1: Water and nature
Remco van Ek, remco.vanek@deltares.nl

## Slide 2: Content
Introduction on myself
Nature protection in the Netherlands
Nature and water quantity: desiccation
Nature and water quality
Nature and climate change
Ecosystem services, management
Knowledge development
Lessons learned

## Slide 3: 1. Introduction on myself
Biologist, University of Amsterdam
Academic background: system ecology, physical geography
Tropical Forest Ecology
Atmospheric deposition on Dutch forest
Professional background: Nation wide policy analysis on groundwater dependent terrestrial ecosystems
Project leader DEMNAT
National Research Program on desiccation
Projects on groundwater dependent ecosystems (values, impact)
Implementation of groundwater aspects within the WFD
Sr Advisor/ Researcher / Program manager at Deltares (Fresh water supply)

## Slide 4: 2. Nature protection in the Netherlands
What kind of groundwater dependent nature in the Netherlands?
Ecosystem types
wet pastureland
bog
fen
heath land*
coastal dunes*
forest*
* = incl. dry types
ponds
wet heather/bogs

## Slide 5: 2. Nature protection in the Netherlands
What kind of groundwater dependent nature in the Netherlands?
Ecosystem types
wet pastureland
bog
fen
heath land*
coastal dunes*
forest*
* = incl. dry types
peatlands
brook valleys

## Slide 6: 2. Nature protection in the Netherlands
Groundwater dependent nature in NL
Botanical conservation values

## Slide 7: 2. Nature protection in the Netherlands
1905 – First nature protection area: Naardermeer
Jac P Thijsse

## Slide 8: 2. Nature protection in the Netherlands
2010
Natuurmonumenten (750.000 members): 355 areas, ~1000 km2
Provincial Landscapes (300.000 members): 800 areas, ~1000 km2
Staatsbosbeheer (government agent): 137 areas, 2600 km2

## Slide 9: 2. Nature protection in the Netherlands
Habitat directive
Bird directive
National nature conservation areas

## Slide 10: 2. Nature protection in the Netherlands
Ecological Main Framework – 7200 km2

## Slide 11: 3. Nature and water quantity: desiccation
Since 1950’s
Agriculture (drainage, irrigation, manure)
Abstractions (increase 300 -> 1300 Mm3/yr)
Decrease in recharge
  Increase in urban area – sewage systems
  Increase in forested areas – increase in evapotranspiration
  Increase in high yield crops – increase in water consumption

## Slide 12: 3. Nature and water quantity: desiccation
Hydrological impacts
Decrease in phreatic groundwater level
  Approx. 30 cm over large areas
  Locally > 1 m (pumping wells)
Decrease in hydraulic head
  Decrease in upward seepage flux
Decrease in water levels in lower part of NL
  Increase inlet of ‘system alien’ water
  Adverse effects on water quality

## Slide 13: 3. Nature and water quantity: desiccation
Inundation
Regional
upward seepage
Local
upward seepage
Infiltration
Downstream
Upstream
High sedge vegetation
Caltha pal. meadow
Juncus vegetation
Low sedge vegetation
Wet heathland
Moist heathland
Dry heathland

## Slide 14: 3. Nature and water quantity: desiccation
Botanical composition
Vegetation competition
Plant physiology
Aeration
Moisture supply
Acidity
Nutrient status
Moisture content
Capillary
properties
Lime content
Soil fertility
Fertilitzation
Surface water
quality
Groundwater
quality
Groundwater
level
Upward
seepage
Inundation
Hydrology
Soil
Management
Site conditions

## Slide 15: 3. Nature and water quantity: desiccation
Hydrological impacts  site conditions
HYDROLOGICAL
CHANGE
PHYS. SIOL
PROCESS
ENVIRONMENTAL
STRESS
Acidification
 moisture supply
Lowering of the
groundwater
level
Desiccation
Eutrophication
 aeration

mineralization
 oxidation processes
Increased influence of
rainwater

## Slide 16: 3. Nature and water quantity: desiccation
Ecological impacts
75% of all nature protection areas are moderate or severely affected
Some effects are irreversible…
Upward seepage

## Slide 17: 3. Nature and water quantity: desiccation
Ecological impacts
75% of all nature protection areas are moderate or severely affected
Some effects are irreversible…
Infiltration

## Slide 18: 4. Nature and water quality
Since WWII
Increase intensive agriculture
Increase in number of cows, pigs  manure
Eutrophication of surface waters  Alga bloom (Microcystes), Duck weed

## Slide 19: 4. Nature and water quality
Water Framework Directive (2000/60/EC)

## Slide 20: 4. Nature and water quality
Since WWII
4. NO3 pollution upper groundwater
50 mg/l = Threshold value
Geen data
0 - 25
25 -50
50 - 100
100 - 150
> 150
Nitrate conc in upper groundwater
mg/l
NO3
FeS
Fe
SO4
N2 (g)
Fe3PO4 + SO4 + H2O
 Fe2+ + PO4(aq) + H2S
NO3 can lead to high SO4 load!!!

## Slide 21: 4. Nature and water quality
Interaction between groundwater and surface water:
Upper groundwater
Rapid discharge
Base flow
Moderate discharge
Deep groundwater
Shallow groundwater
Class 1: 100% base flow
Class 2: 0-20% rapid discharge
Class 3: 20-40% rapid discharge
Class 4: 40-60% rapid discharge
Class 5: 60-80% rapid discharge
Class 6: 80-90% rapid discharge
Class 7: 90-100% rapid discharge

## Slide 22: 4. Nature and water quality
Interaction between groundwater and surface water:

## Slide 23: 5. Nature and climate change
What will happen to our climate? In 2050? 2100?

## Slide 24: 5. Nature and climate change

## Slide 25: 5. Nature and climate change

## Slide 26: 5. Nature and climate change
1. Envelop models
2. Models on Site conditions
3. Expert judgement
vulnerability
scetch map
Different approaches for impact assessment

## Slide 27: 5. Nature and climate change
Witte et al., 2012 Ecohydrological effects of climate change
Groundwater independent ecosystems (dry forest, heather, dunes)
Increase in drought stress
Increase in fire risk
More open vegetation
Increase in warm tolerant species
Rainfed wet ecosystems (bogs, wet heather, ponds)
W+ for peat bogs possibly critical (T too high, P-ET too low, dGXG too large)
Wet heather more desiccation, more mineralisation
Ponds: Increase in dry fall, more mineralisation

## Slide 28: 5. Nature and climate change
Witte et al., 2012 Ecohydrological effects of climate change
Ecosystems fed by upward seepage and surface water (brook valleys, fens, wet dune valleys)
Regional upward seepage areas relatively robust
Damage due to groundwater lowering (mineralisation)
Upward seepage increase?
In fens damage due to groundwater lowering, increase in mineralisation and more inlet of system alien water
Small surface waters (brooks, streams, ditches, lakes, ponds)
More dry fall (upper part of streams)
Increase in eutrophication ditches / lakes due to higher temp.
More inundation along streams (eutrophication )
More salinisation

## Slide 29: 5. Nature and climate change
G
Wetter conditions
Increase in weather extremes
Some change in moisture deficit and water demand
W+
Wetter winters: more flooding
More frequent dry summers, lowering of water levels: more desiccation
Higer temperatures, stronger fluctuation in groundwaterlevels, increased mineralisation: peat areas under stress
Upward seepage increase/decrease? Effect on vegetation cover?
Big increase in moisture deficit and water demand
Scetch map of
ecohydrological
effects
Witte et al., 2012

## Slide 30: 5. Nature and climate change
Climate adaptation: climate buffers
Potential water storage areas
Water conservation
Water storage
Water release
Retain Store Remove
Water management for the 21st century

## Slide 31: 5. Nature and climate change
Climate adaptation: climate buffers
brace profile
Current situation
New situation: low storage
New situation: high storage

## Slide 32: 5. Nature and climate change
Climate adaptation: climate buffers
Effects of water storage on nature?
Runhaar et al., 2004
Inundation
Input of toxic
compounds
Input of sulphate
through surface water
Increased mortality
due to oxygen deficiency
(drowning)
Oxygen deficit
Change in
species
composition
Water storage
Input of nutriënts
(NPK) through surface
water
Input of nutriënts
(NPK) through sediment
Input basics
through sediment
Input bicarbonate
through sediment
In/output of
Salt
Increased mortality
due to intoxication
Increased production
vegetation (eutrophication)
Increase pH
(alkalinity)
(salinisation/sweetening)
Reduction
sulphate
reduction
H2S-
Formation
P-mobilistation
Decomposition of
organic matter

## Slide 33: 5. Nature and climate change
Climate adaptation: climate buffers
New nature areas: Yes please, but…

## Slide 34: 5. Nature and climate change
Climate adaptation: climate buffers
Existing nature areas:
No, unless…

## Slide 35: 6. Ecosystem services, management
What is the value of nature / ecosystems?

## Slide 36: 6. Ecosystem services, management
What is the value of nature / ecosystems?
Intrinsic value ( - )
Use value ( € )
Non use value ( € )
Total economic value
Ecosystems Goods & Services

## Slide 37: 6. Ecosystem services, management

## Slide 38: 6. Ecosystem services, management
Framework for ecosystem assessment (Ranganathan, 2008)
Payement for
Ecosystem Services:
the beneficiary
pays

## Slide 39: 6. Ecosystem services, management

## Slide 40: 6. Ecosystem services, management

## Slide 41: 7. Knowledge development
Too much
Too dirty
Nature &
Watersystems
Too little
Water scarcity
& droughts
Floods
Water pollution
Man & Society

## Slide 42: 7. Knowledge development
objectives
measures
Watersystem
analysis
monitoring

## Slide 43: 8. Lessons learned
xx